## Slide 1
IEEE WEEK 2026 · MECH. ENGG.
Introduction to Drone Technology
Turn code into motion. 13 Oct · MPH · 9:30–12:30
ESP32 · 500 Hz
AO3400 drivers
6S brushless FPV
M1
M2
M3
M4
ESP32
MPU-6050
Notes: Welcome, everyone. Today we walk through how to build, fly and tune a drone from scratch, and we start with a confession: our first prototype never flew. It just skated across the floor. Our second one climbed straight up. By the end of this session you will know exactly what changed between the two, and how every layer of a quadcopter works, from the physics to the firmware to a full 6S racing build.

## Slide 2
02 / ROADMAP
Five stops from physics to flight
01
Flight physics
How 4 motors steer roll, pitch, yaw and thrust
SLIDES 3–4
02
Micro build
Parts, the driver that failed, and the MOSFET fix
SLIDES 5–9
03
Firmware
500 Hz loop, PID, motor mixer and radio links
SLIDES 10–12
04
Pro FPV stack
Brushless motors, DShot and 6S power
SLIDES 13–17
05
Fly safely
Bench rules, flight modes, PID tuning
SLIDES 18–20
Build, Fly & Tune a Drone from Scratch
02 / 21
Notes: Here is the route for today, five stops climbing from theory to flight. First the physics of how four motors steer a quad. Then our micro build on an ESP32, including the driver that failed and the MOSFET fix. Then the firmware: the 500 hertz loop, the PID controller, the motor mixer and the radio links. Then we scale up to a five-inch FPV racer with brushless motors, DShot and 6S power. And finally how to fly safely: bench rules, flight modes and PID tuning.

## Slide 3
03 / FLIGHT PHYSICS
How four motors steer a quad
FRONT ↑
M1 · FL
M2 · FR
M3 · RR
M4 · RL
CW
CCW
CW
CCW
Roll
lean right
M1 + M4 (left side) spin faster
Pitch
nose down
M3 + M4 (rear pair) spin faster
Yaw
turn right
M2 + M4 (CCW pair) spin faster
Throttle
climb
All four together; aim for ≈ 2:1 thrust
Filled motor = spins faster · Body frame: X forward, Y right, Z down
03 / 21
Notes: A quadcopter has no rudder and no flaps. It steers only by changing how fast each motor spins. Motor one is front left and spins clockwise, motor two is front right and spins counter-clockwise, three is rear right clockwise, four is rear left counter-clockwise. To roll right, the left pair, motors one and four, speeds up. To pitch nose down and fly forward, the rear pair, three and four, speeds up. Yaw is the clever one: speed up the counter-clockwise pair, two and four, and their reaction torque twists the frame to the right. Throttle is all four together. To hover you only need thrust equal to weight, but you want about two to one so there is margin left over for control.

## Slide 4
04 / TWO MACHINES
Same physics, very different machines
Our micro quad
45–60 g
all-up weight
1S LiPo · 3.7 V
BRAIN
MOTORS
DRIVER
RADIO
GOAL
ESP32, Arduino C++ we wrote
8520 coreless brushed
4 × AO3400 MOSFETs, PWM
ESP-NOW remote + phone app
Learn every layer
5-inch FPV racer
550–680 g
all-up weight
6S LiPo · 22.2 V
BRAIN
MOTORS
DRIVER
RADIO
GOAL
STM32 F7/H7 + Betaflight
2207 brushless, 1750–1960 KV
4-in-1 ESC, DShot600
ExpressLRS, 2.4 GHz
Speed and agility
Build, Fly & Tune a Drone from Scratch
04 / 21
Notes: The physics is the same for every quad, but the machines can be very different. Our micro quad weighs forty-five to sixty grams, runs on a single 3.7 volt cell, uses an ESP32 with firmware we wrote ourselves in Arduino C plus plus, coreless brushed motors and four tiny MOSFETs. Its goal is to teach every layer. A five-inch FPV racer weighs ten times as much, runs on six cells at 22.2 volts, uses an STM32 flight controller running Betaflight, brushless motors, a four-in-one ESC speaking DShot600, and an ExpressLRS radio. Its goal is raw speed and agility.

## Slide 5
05 / MICRO BUILD
What is on our 50-gram quad
ESP32
ESP32 DevKit V1
Dual-core 240 MHz; one core runs the 500 Hz flight loop
MPU-6050 IMU
3-axis gyro + accelerometer, I²C at 400 kHz, at the CG
AO3400 driver × 4
One low-side MOSFET per motor, 16 kHz PWM from the ESP32
8520 coreless motor × 4
8.5 × 20 mm, about 5 g each, turning 55 mm props
1S LiPo power
3.7 V cell, TP4056 USB charger, 5 V boost keeps the ESP32 stable, voltage read on GPIO 34 (100k / 100k divider)
Dashed teal outline = battery under the frame · Orange squares = MOSFET drivers
05 / 21
Notes: Here is everything on our fifty-gram quad. The ESP32 DevKit is the brain; it is dual core at 240 megahertz, and one core is dedicated to the 500 hertz flight loop. The MPU-6050 gives us a three-axis gyro and accelerometer over I2C at 400 kilohertz, and it sits at the centre of gravity so it does not feel extra motion when the frame rotates. Each 8520 coreless motor is eight and a half by twenty millimetres, about five grams, turning 55 millimetre props. Each one is switched by its own AO3400 MOSFET at 16 kilohertz. Power comes from a single LiPo cell with a TP4056 USB charger, a 5 volt boost so the ESP32 never browns out, and a 100k by 100k divider so we can read the battery voltage on GPIO 34.

## Slide 6
06 / THE ROADBLOCK
Prototype 1 never left the floor
ESP32, MPU-6050, four 8520 motors, a 1S LiPo, and two DRV8833 H-bridge boards driving the motors.
At full throttle the drivers overheated and cut out. The quad skated across the floor instead of lifting off.
< 2.7 V
reached the motors (measured)
from a battery rated 3.7 V
props spinning, no lift
Phase 2 · Micro build
06 / 21
Notes: Now the story of prototype one. Same ESP32, same IMU, same motors, same battery, but the motors were driven by two DRV8833 H-bridge boards. At full throttle the drivers overheated and cut out, and the quad just skated across the floor. When we put a multimeter on the motor terminals we measured less than 2.7 volts, from a battery rated 3.7. Somewhere we were losing a whole volt. Let us find out where.

## Slide 7
07 / DIAGNOSIS
Where the missing volt went
1S LiPo
3.7 V nominal
3.7 V
I ≈ 3.5 A
DRV8833
≈ 360 mΩ
< 2.7 V
M
8520 motor
Lost in the chip:
3.5 A × 0.36 Ω ≈ 1.3 V
burned as heat
Driver limit
1.5 A RMS, 2 A peak per channel (datasheet)
Motor demand
8520s pull 3.5–4.2 A at full throttle
Protection trips
Over-current and thermal shutdown cut the motors
Lesson: H-bridge ICs suit 0.5–0.8 A toy-car motors. Coreless drone motors need a bigger switch.
DRV8833 figures: TI datasheet (typical RDS(on) high + low side). Motor current: typical 8520 stall figure.
07 / 21
Notes: Follow the current. The battery delivers 3.7 volts, but inside each DRV8833 channel the current passes through a high-side and a low-side transistor, about 360 milliohms in total according to the TI datasheet. Coreless motors at full throttle pull three and a half to four amps. Ohm's law says three and a half amps times 0.36 ohms is about 1.3 volts, burned inside the chip as heat. On top of that, the DRV8833 is rated for 1.5 amps RMS and 2 amps peak per channel, so its over-current and thermal protection kept cutting the motors. The lesson: H-bridge ICs are made for half-amp toy car motors that need to run in both directions. A drone motor only spins one way and needs much more current.

## Slide 8
08 / THE FIX
One MOSFET per motor
M
ESP32 GPIO
VBAT 3.7 V
AO3400
10 kΩ
SS24
8520
PWM
GND
1
2
3
M1 GPIO32 · M2 GPIO25 · M3 GPIO33 · M4 GPIO26
16 kHz, 12-bit PWM from the ESP32 LEDC timers
1
AO3400 N-channel MOSFET
Logic-level: a 3.3 V gate turns it fully on. Tens of mΩ, 5.7 A continuous.
2
10 kΩ gate pull-down
Holds the gate low while the ESP32 boots, so motors cannot twitch at power-up.
3
SS24 Schottky diode (40 V, 2 A)
Gives the motor current a path when the FET turns off, so no voltage spike.
Low-side switch, ×4. Pins from Drone/src/config.h
08 / 21
Notes: The fix is beautifully simple: one N-channel MOSFET per motor, used as a low-side switch. The motor sits between the battery and the MOSFET's drain, and the ESP32 drives the gate directly with PWM. Part one, the AO3400, is logic-level, so a 3.3 volt gate turns it fully on with only tens of milliohms of resistance, and it is rated 5.7 amps continuous. Part two, a 10 kilohm pull-down on the gate, keeps the motor off while the ESP32 boots and its pins are floating. Part three, the SS24 Schottky diode across the motor, catches the motor's stored energy when the MOSFET switches off, so there is no voltage spike to kill the transistor. The pins are GPIO 32, 25, 33 and 26 for motors one to four, driven at 16 kilohertz with 12-bit resolution.

## Slide 9
09 / BEFORE VS AFTER
Same motors, new driver: it flies
DRV8833 H-bridge
✕ FAILED
≈ 360 mΩ
1.5 A RMS · 2 A peak
< 2.7 V (measured)
Thermal shutdown
Skated on the floor
RESISTANCE
CURRENT
AT MOTOR
HEAT
RESULT
AO3400 MOSFET
✓ FLIES
Tens of mΩ (≈ 10× less)
5.7 A continuous
3.65 V+ (measured)
Runs cool
Climbs at ~55 % throttle
Same motors, same battery, same code. Only the driver changed.
Measure the voltage at the motor terminals, not just at the battery.
Build, Fly & Tune a Drone from Scratch
09 / 21
Notes: Here is the comparison. The DRV8833 path was about 360 milliohms; the MOSFET is tens of milliohms, roughly ten times less. The DRV8833 allowed 1.5 amps RMS; the AO3400 handles 5.7 amps continuous. At the motor terminals we measured under 2.7 volts before and over 3.65 volts after. The drivers went from thermal shutdown to running cool, and the quad went from skating on the floor to climbing at about 55 percent throttle. Same motors, same battery, same code. Only the driver changed. The engineering habit to take away is to measure the voltage where the power is used, not just at the battery.

## Slide 10
10 / FIRMWARE
Two cores, one 500 Hz flight loop
CORE 0 · WI-FI + ESP-NOW STACK
Radio receives stick packets from the remote or the phone app
CORE 1 · FLIGHT TASK · 500 Hz
setpoints
Read IMU
Fuse
PID
Mix
PWM out
gyro + accel, I²C
attitude estimate
angle → rate loop
Quad-X mixer
4 motors, 16 kHz
CORE 1 · loop() · LOW PRIORITY
Commands
Telemetry
Battery + LED
Motor watchdog
serial + web page
+ blackbox log
voltage, status
task silent 50 ms → cut
Rule: only the flight task touches I²C and the motors; the rest uses locked shared data.
Arduino framework on FreeRTOS · no external libraries
10 / 21
Notes: Now the firmware. The ESP32 has two cores. Core zero runs the Wi-Fi and ESP-NOW radio stack, which receives stick packets and turns them into setpoints. Core one runs our flight task every two milliseconds, five hundred times a second, at high priority: read the IMU, fuse the readings into an attitude estimate, run the PID controller, mix the corrections into four motor outputs, and write the PWM. Also on core one, at low priority, the normal Arduino loop handles serial and web commands, telemetry and the blackbox log, battery and LED, and a watchdog that cuts the motors if the flight task goes silent for fifty milliseconds. The rule that keeps this safe is that only the flight task ever touches I2C and the motors; everything else talks to it through small locked shared buffers.

## Slide 11
11 / CONTROL LOOP
Inside every 2 ms tick
Pilot stick
Angle loop
Rate loop
Mixer
Motors
±500 units
P × 4
PID vs gyro
Quad-X
M1–M4
≤ 30°
≤ 200°/s
r, p, y
IMU + complementary filter
angle estimate
gyro rate
Complementary filter, α = 0.995
angle = 0.995 × (angle + gyro × dt) + 0.005 × accel_angle
Gyro is smooth but drifts. Accel knows “down” but is noisy. Accel is ignored outside 0.8–1.2 g.
Quad-X mixer (mixer.cpp)
m1 = t + r + p − y // FL CW m2 = t − r + p + y // FR CCW m3 = t − r − p − y // RR CW m4 = t + r − p + y // RL CCW
D acts on measurement · I frozen below 15 % throttle
t = throttle, r/p/y = roll/pitch/yaw corrections · values from Drone/src/config.h
11 / 21
Notes: Inside each two millisecond tick, the controller is a cascade of two loops. The pilot's stick becomes a target angle, at most thirty degrees. The outer angle loop compares that with the estimated angle and multiplies the error by four to get a target rotation rate, capped at two hundred degrees per second. The inner rate loop is a full PID that compares the target rate with what the gyro measures. The mixer then turns roll, pitch and yaw corrections into four motor commands. The angle estimate comes from a complementary filter: we trust the gyro 99.5 percent because it is smooth, and the accelerometer half a percent because it knows which way is down but is noisy. If the accelerometer reads far from one g, during a hard manoeuvre, we ignore it. Two more details: the D term acts on the measurement so a stick jump does not kick the motors, and the I term is frozen below fifteen percent throttle so it does not wind up on the ground.

## Slide 12
12 / RADIO LINKS
Three ways to talk to the drone
Handheld remote
ESP-NOW on Wi-Fi channel 1 Peer-to-peer, no router 13-byte packet (below)
Wi-Fi AP
192.168.43.42
ESP-Drone phone app
UDP to 192.168.43.42 : 2390 Zero throttle, then raise to arm
Web dashboard
Live telemetry, PID tuning, bench tests while disarmed
ESP-NOW packet · 13 bytes, packed
magic
seq
throttle
roll
pitch
yaw
flags
throttle 0 – 1000 sticks −500 … +500 flags bit 0 = arm switch
Failsafe: no packet for 500 ms while armed → motors disarm.
Packet struct is duplicated in Drone/src/radio.h and Transmitter/Transmitter.ino
12 / 21
Notes: There are three ways to talk to this drone. A handheld remote, another ESP32, sends ESP-NOW packets on Wi-Fi channel one, peer to peer, no router needed. Each packet is thirteen bytes: a magic number, a sequence counter, throttle from zero to a thousand, and roll, pitch and yaw from minus five hundred to plus five hundred, plus a flags byte where bit zero is the arm switch. Second, the drone runs its own Wi-Fi access point at 192.168.43.42, so the ESP-Drone phone app can fly it over UDP port 2390. To arm from the app you bring throttle to zero after connecting and then raise it. Third, a web dashboard shows live telemetry, lets you tune PID gains, and runs bench tests while disarmed. Whatever the link, if no packet arrives for 500 milliseconds while armed, the drone disarms itself.

## Slide 13
PHASE 04 OF 05
04
Scaling up: the 5-inch FPV racer
Same physics. Everything else gets bigger, faster and digital.
Brushless motors replace brushed
An ESC with digital DShot replaces the MOSFET
6S LiPo: 22.2 V instead of 3.7 V
13 / 21
Notes: That is our micro quad. Now let us scale up to a five-inch FPV racer. The physics does not change at all. What changes is everything around it: brushless motors instead of brushed ones, an electronic speed controller speaking a digital protocol instead of a simple MOSFET, and a six-cell battery at 22.2 volts instead of a single 3.7 volt cell.

## Slide 14
14 / FPV STACK
Inside a 5-inch racer, layer by layer
6S LiPo
Receiver
Flight controller
4-in-1 ESC
Carbon frame + motors
exploded view · not to scale
6S LiPo battery
ExpressLRS receiver
Flight controller
4-in-1 ESC
Frame + motors
22.2 V nominal, ~1300 mAh, 120 C
2.4 GHz, up to 1000 packets/s (short range)
STM32 F7/H7, Betaflight, ICM-42688 gyro
45–60 A per motor, DShot600 + RPM telemetry
5-inch carbon, 2207 motors at 1750–1960 KV
Typical build · Betaflight runs an 8 kHz gyro + PID loop on F7/H7
14 / 21
Notes: Here is a racer taken apart, layer by layer. On top, a 6S LiPo, typically around 1300 milliamp hours with a high C rating. Below it the ExpressLRS receiver on 2.4 gigahertz, which can send up to a thousand packets a second at short range, trading rate for range. Then the flight controller, an STM32 F7 or H7 running Betaflight with a low-noise gyro such as the ICM-42688, running its gyro and PID loop at eight kilohertz, sixteen times faster than ours. Under that, a four-in-one ESC rated 45 to 60 amps per motor, speaking DShot600. At the bottom, a five-inch carbon frame with 2207 motors, usually 1750 to 1960 KV on six cells.

## Slide 15
15 / MOTORS
Brushed vs brushless, and what KV means
Brushed · our 8520
Brushes rub a commutator, so they wear out
Plain DC: our MOSFET switches it on and off
Cheap; fine for quads under about 60 g
Brushless · 2207 racer motor
No brushes: the ESC switches 3 phases
12 coils, 14 magnets (12N14P)
Bearings are the only part that wears
Reading the name “2207”
22 mm stator diameter
07 mm
stator, side view · wider = torque, taller = top-end RPM
KV = RPM per volt, with no load
1960 KV × 22.2 V (6S)
≈ 43,500 RPM
Under load it spins slower. 6S builds use lower KV (1750–1960), 4S builds higher (2400+).
Build, Fly & Tune a Drone from Scratch
15 / 21
Notes: Our brushed motors have carbon brushes that rub on a commutator, so they wear out, but they are cheap and need only simple on-off PWM, which is perfect under sixty grams. Brushless motors have no brushes; the ESC switches three phases electronically, a typical racer motor has twelve coils and fourteen magnets, and only the bearings wear. The name 2207 is just the stator size: 22 millimetres in diameter, 7 millimetres tall. Wider gives more torque, taller gives more top-end speed. KV means RPM per volt with no load, so a 1960 KV motor on a 22.2 volt pack spins at about 43,500 RPM unloaded, and slower under the load of a propeller. That is why six-cell builds use lower KV and four-cell builds use higher KV.

## Slide 16
16 / ESC PROTOCOL
DShot: throttle sent as a number
Old way · PWM / OneShot
throttle = how long the pulse stays high; drifts, needs calibration
low
high
DShot600 · one 16-bit frame
1
0
0
0
0
0
1
0
1
1
0
0
0
1
1
0
throttle · 11 bits · e.g. 1046
T
CRC · 4 bits
48–2047 = throttle · 1–47 = commands · T = telemetry request
26.7 µs
per frame: 16 bits at 600 kbit/s
Bidirectional DShot
The ESC replies with motor RPM on the same wire. Betaflight uses it to notch out motor noise.
Active braking (“damped light”)
The ESC brakes the prop when throttle drops, so the quad reacts and settles faster.
Example frame: throttle 1046, telemetry 0, CRC = (v ⊕ v≫4 ⊕ v≫8) & 0xF
16 / 21
Notes: Older ESC protocols encoded throttle as the width of a pulse, between one and two milliseconds. That analog timing drifts and needs calibration. DShot sends throttle as a number. Each frame is sixteen bits: eleven bits of throttle, where 48 to 2047 is throttle and 1 to 47 are special commands, one bit to request telemetry, and a four-bit checksum, so corrupted frames are thrown away. At 600 kilobits per second a frame takes just under 27 microseconds. Two extras matter for flying. Bidirectional DShot lets the ESC send motor RPM back on the same wire, and Betaflight uses that to place notch filters exactly on the motor noise. Active braking lets the ESC slow the prop down instead of letting it coast, so the quad responds and settles faster.

## Slide 17
17 / POWER
Why racers moved from 4S to 6S
4S · 14.8 V NOMINAL
68 A
needed for a 1000 W punch-out
6S · 22.2 V NOMINAL
45 A
for the same 1000 W: less heat, less sag
I = P ÷ V. Heat in wires and cells grows with I²R, so a third less current matters a lot.
How much can a pack give?
max current = capacity × C
1.3 Ah × 120 C = 156 A
Pull more and the cells puff up and age fast.
Protect the electronics
Low-ESR cap on the ESC pads, e.g. 1000 µF, rated 35 V+ (50 V gives margin on 6S)
A TVS diode clamps voltage spikes from active braking
Full charge: 4.2 V per cell (6S = 25.2 V) · storage ≈ 3.8 V per cell
17 / 21
Notes: Why did racers move from four cells to six? Power is voltage times current. For the same thousand-watt punch, a 4S pack at 14.8 volts must deliver about 68 amps, while a 6S pack at 22.2 volts needs only about 45. Heat in the wires and in the cells grows with current squared times resistance, so a third less current means far less heat and far less voltage sag. To know what a pack can deliver, multiply capacity by C rating: a 1.3 amp-hour pack rated 120 C gives 156 amps continuous. Pull more and the cells puff up and age quickly. And protect your electronics: a low-ESR capacitor across the ESC pads, for example a thousand microfarads rated 35 volts or more, with 50 volts giving extra margin on 6S, and optionally a TVS diode to clamp the spikes that active braking pushes back into the battery line.

## Slide 18
18 / BENCH SAFETY
Four rules before every power-up
1 · Props off on the bench
Never power motors with props fitted. A surprise spin-up cuts in milliseconds.
2 · Smoke stopper on first power-up
A resettable fuse in the battery lead trips before a short can burn the board.
3 · Check for shorts first
Multimeter across VBAT and GND before the battery goes in: no near-zero reading.
4 · Test the failsafe
While disarmed, switch the radio off. The drone must stay disarmed.
Our firmware enforces it too
Motor tests stay locked until you type props off (unlock lasts 5 minutes)
Motor tests and setting changes run only while disarmed
No radio packet for 500 ms while armed → the drone disarms itself
Flight task silent for 50 ms → loop() cuts the motors
Never weaken these without a reason.
Treat every quad on the bench as armed.
18 / 21
Notes: Before anything flies, four rules. First, props off on the bench, always; a motor that spins up unexpectedly can cut you in milliseconds. Second, use a smoke stopper, a resettable fuse in the battery lead, the first time you power a new build, so a short trips the fuse instead of burning the board. Third, check for shorts with a multimeter across battery positive and ground before plugging in; you should never see a near-zero reading. Fourth, test the failsafe: with the drone disarmed, switch the radio off and confirm the drone stays disarmed. Our own firmware enforces the same ideas. Motor tests are locked until you type props off, which unlocks them for five minutes. Tests and settings changes only run while disarmed. No radio packet for 500 milliseconds while armed disarms the drone, and if the flight task stops for 50 milliseconds, the main loop cuts the motors.

## Slide 19
19 / FLIGHT MODES
Angle mode vs Acro mode
START HERE
30°
Angle · self-levelling
Stick sets the tilt angle (ours: max 30°)
Let go and it levels itself
Uses gyro + accelerometer
FLIPS + RACING
e.g. 670°/s at full stick
Acro · rate mode
Stick sets how fast it rotates
Let go: it holds its attitude, even inverted
Gyro only; accelerometer ignored
Learn in Angle, then practise Acro in a simulator before real flips.
Our ESP32 firmware flies in Angle mode (MAX_ANGLE_DEG = 30)
19 / 21
Notes: There are two main ways a flight controller interprets your sticks. In Angle mode, the stick sets a tilt angle, at most thirty degrees on our firmware, and when you let go the drone levels itself using both the gyro and the accelerometer. That is how our ESP32 quad flies, and it is where every beginner should start. In Acro or rate mode, the stick sets how fast the drone rotates, for example 670 degrees per second at full stick, and when you let go it simply holds whatever attitude it is in, even upside down. It uses only the gyro. That is what makes flips and racing possible. Learn in Angle, then practise Acro in a simulator before you try real flips.

## Slide 20
20 / PID TUNING
What each PID gain does
Response to a sudden stick move
illustrative
time →
target
too much P
tuned
too little P
P
Stiffness · reacts to the error now
Too high: fast ringing, buzzing motors Too low: sloppy, drifts off the line
I
Memory · fixes error that lingers
Too high: slow wobble after a move Too low: will not hold its angle in wind
D
Damping · brakes the motion
Too high: amplifies noise, hot motors Too low: overshoot, prop-wash shake
1 · P up until it rings, then −15 %
2 · D up until overshoot stops
3 · I up until it holds angle
Start with I and D at zero. Check motor temperature after every D change. Our gains tune live from the web page.
20 / 21
Notes: Finally, tuning. The graph is illustrative: it shows how the drone responds to a sudden stick movement. P is stiffness; it reacts to the error right now. Too much P and the drone overshoots and rings, with buzzing motors. Too little and it feels sloppy and drifts off line. I is memory; it fixes errors that linger, like wind or an off-centre battery. Too much gives a slow wobble after a move; too little and it will not hold its angle. D is damping; it brakes the motion before it overshoots. Too much amplifies sensor noise and makes motors hot; too little gives overshoot and prop-wash shaking. The method: start with I and D at zero, raise P until it rings and back off about fifteen percent, raise D until the overshoot stops while checking motor temperature, then raise I until it holds its angle. On our drone you can do all of this live from the web page.

## Slide 21
21 / WRAP-UP
Measure first, then design.
YOU CAN NOW
✓ Explain how four motors steer a quad
✓ Choose a motor driver from its datasheet
✓ Read a 500 Hz loop: IMU → PID → mixer
✓ Spec a 6S racer and tune PID safely
NEXT UPGRADES
GPS rescue
Fly home by itself if the link drops
HD digital video
Low-latency HD goggles instead of analog
Optical flow + barometer
Hands-free hover, even indoors
Questions? Then go build one.
21 / 21
ATTENDEES ONLY
Firmware, slides + speaker notes
github.com/ara-aras/esp32-mini-drone
Notes: If you remember one thing from today, let it be this: measure first, then design. Our drone did not fly until we measured the voltage at the motors and found the real problem. You can now explain how four motors steer a quad, choose a motor driver from its datasheet, read a 500 hertz control loop from IMU to PID to mixer, and spec a 6S racer and tune it safely. Good next upgrades are GPS rescue, so the drone flies home if the link drops, HD digital video, and optical flow with a barometer for hands-free hovering indoors. Questions? Then go build one. One last thing: the QR code is the repo with the firmware, these slides and my speaker notes. It is only for the people in this room; I am not posting the link anywhere else, so anyone who skipped has to ask one of you.